## Slide 1: IcUB and R1 Hardware and infrastructure
by the IT point of view

## Slide 2: What are we going to see?
Hardware components
Networking
Software components

## Slide 3: Which robotic setups?
iCub (black, purple, green, iCub3)
R1 (mk1 and mk2)

## Slide 4: iCub Setup
There is not a standard for components, each setup is different
The same component (i.e. wifi router) can be different in vendor and model among setups
Setups are not steady, components change to follow new needing (it’s research, baby!)
Changes in HW components may requires changes in SW configuration
So, instead of describing each setup in detail, we’ll see an the «ideal» setup (iCub3) and we’ll describe hardware components generally
iCub Hardware components 1/4

## Slide 5: The past
iCub Hardware components 2/4

## Slide 6: The future – iCub3
Designed to be portable:
Small desktop server
Small desktop network switch
Wifi router (similar to IIT wifi infrastructure)
Powerfull laptop PCs with CUDA-capable GPU
CUDA box (to be attached to laptops)
iCub head: COMexpress embedded PC with ssd Hard Drive, WiFi and Bluetooth
iCub Hardware components 3/4

## Slide 7: The present – other setup
Black iCub
7U rack with power supply and network switch (rack model)
Small desktop server
New GPU-equipped Alienware laptop
CUDA workstation
iCub head – PC104 diskless (OS on USB)
Purple iCub
7U rack with power supply, network switch (rack model) and main server (rack model), CUDA workstation (rack mounted)
Old model laptops
iCub head – COMexpress with SSD disk and WiFi
iCub Hardware components 4/4
Green iCub
7U rack with power supply, network switch (rack model) and main server (rack model)
Old model laptops and new GPU-equipped Alienware
Cuda Workstation
Wifi router
iCub head – COMexpress with SSD disk, Bluetooth and WiFi

## Slide 8: R1 Setup
There are only 2 versions: old (mk1) and new (mk2), with small differences in HW components (the bigger changes are in mechanics)
Usually, new hardware is added to the newer setup (mk2)
The situation is more stable than iCub setup and the we’ll see in details newer version.
R1 Hardware components 1/

## Slide 9: R1 MK2 – on board
R1 Hardware components 2/
The face PC – an ARM based embedded PC with OS (Ubuntu) running on SD card that controls face display
The torso PCs – two ARM based embedded PC with OS (Ubuntu) on internal memory and a CUDA-capable GPU
The base PC – an X86 based embedded PC with OS (Ubuntu) running on SSD drive (PCI-X)
Networking – embedded wifi media coverted with 4 ports switch, it can operate in 2 different modes (standalone and client)

## Slide 10: R1 MK2 – external components
Designed to be portable:
Small desktop network router with wifi
Laptop PCs
Powerful laptop PCs with CUDA-capable GPU
CUDA box (to be attached to laptops)
R1 Hardware components 3/4

## Slide 11: R1 MK1 – differences
Less hardware:
On board - Single embedded PCs in the robot torso
NO laptop PCs with CUDA-capable GPU
NO CUDA box
R1 Hardware components 4/4

## Slide 12: iCub and R1 networking
Physical connections
Logical connections
Sockets and cables
Protocols and routing

## Slide 13: iCub Physical connections
There are small but important differences among setups, here we describe the general principles, a «live» tour of setups will explain details and differences.
There are two operative modes:
iCub Networking 1/4
Home
Abroad
Uses the IIT networking infrastructure and desk sockets
Uses the setup networking infrastructure and (long) cables

## Slide 14: Home operative mode
This mode uses the IIT networking infrastructure (switches, wifi) to connect robot components, which have to be connected to network socket on the desks
iCub Networking 2/4
front
Rack network plugs
7
U ack
–
«Power»
Virtual Server
–
running vmWare ESX
(
1
U
)
·
Nork Switch
24
ports
(
1
U
)
·
12
V Power Supply
(
2
U
)
·
40
V Power supply
(
2
U
)
·
Rack Network plugs
(
1
U
)
back
The INTERNAL socket must be connected to an Robot VLAN socket on desks
The EXTERNAL socket must be connected to a normal socket on desks

## Slide 15: Abroad operative mode
This mode uses the setup switch (switches, wifi) to connect robot components, it is used while travelling
iCub Networking 3/4
front
Rack network plugs
7
U ack
–
«Power»
Virtual Server
–
running vmWare ESX
(
1
U
)
·
Nork Switch
24
ports
(
1
U
)
·
12
V Power Supply
(
2
U
)
·
40
V Power supply
(
2
U
)
·
Rack Network plugs
(
1
U
)
back
The INTERNAL socket must be connected to a posrt on the Robot switch
The EXTERNAL socket must be connected to a normal socket (internet connected)

## Slide 16: iCub Logical network connections
iCub Networking 4/4
wifi
laptops
robot
workstations
switch
iCub server
Internet
iCub private subnet 10.0.0.0/24
External (DHCP)
Internal (10.0.0.1)
The iCub server is the default GATEWAY for the robot private subnet.
If its external connection is not active there is no internet connection.

## Slide 17: R1 Physical connections
There are no differences between old and new setup, but the robot can work in 2 different modes:
R1 Networking 1/2
Client (normal)
Standalone
The wifi infrastructure is provided by the wifi router and if the router which also works as gateway to internet. The robot connect to the wifi using onboard wifi, which acts as a client.
The wifi infrastructure is provided by robot onboard switch. There is no internet connection, you can connect to robot machines only by connecting to its wifi. The wifi router must be switched off
With a switch on the robot you can change operative mode (when robot is off)

## Slide 18: R1 Network connections
R1 Networking 2/2
Internet
Wifi router
Laptop (wifi)
robot (wifi)
Laptop (cabled)
R1 private subnet 192.168.100.0/24
WAN (DHCP)
192.168.100.1

## Slide 19: iCub Software components
wifi-equipped robots (all but Blacky) does not mount anymore the NFS repository for code and local_yarp. They have their own copy of code and .local/yarp in the internal HD, this beacuse NFS can be severely harm by the (potential) instability of wifi connection

## Slide 20: R1 Software components
R1 wifi Router
192.168.100.1
Subnet GATEWAY
DHCP server
DNS
NTP server
SSID : r1_SERIAL-wifi (where SERIAL is robot serial number, eg. for robot #001 is r1_001-wifi)
DHCP Server
Start IP address : 192.168.100.100
Maximim number of users : 150
Client lease time : 1440 sec
DNS Server
r1-base 192.168.100.10
r1-torso1 192.168.100.21
r1-torso2 192.168.100.22
r1-face 192.168.100.30
R1 onboard wireless Access Point - STANDALONE
192.168.100.99
NO internet connection
NO DHCP server (use only static IP on clients)
NO DNS
NO server
SSID : r1_SERIAL-wifi (where SERIAL is robot serial number, eg. for robot #001 is r1_001-wifi)
R1 onboard wireless Access Point - CLIENT
192.168.100.99
Connect as a client to the Router wifi infrastructure

## Slide 21: See also..
Further details can be found on:
Setup system configurations repository on Github[1]
Robotology Redmine Knowledge Base[2]
iCub tech internal wiki[3]
iCub project wiki[4]
[1] https://github.com/icub-tech-iit/setup-system-configurations
[2] https://redmine.robotology.eu/easy_knowledge_globals
[3] https://wiki.icub.iit.local/index.php/ICub_setup_enviroment
[4] https://wiki.icub.org